Timer in Linux Kernel

In Linux, kernel keeps track of the flow of time by means of timer interrupts. This timer interrupts are generated at regular timer intervals by using system’s timing hardware. Every time a timer interrupt occurs, the value of an internal kernel counter is incremented. The counter is initialized to 0 at system boot, so it represents the number of clock ticks since last boot.

Kernel timer offers less precision but is more efficient in situations where the timer will probably be canceled before it fires. There are many places in the kernel where timers are used to detect when a device or a network peer has failed to respond within the expected time.

When you want to do some action after some time, then kernel timers are one of the option for you. These timers are used to schedule execution of a function at a particular time in the future, based on the clock tick, and can be used for a variety of tasks.

# Uses of Kernel Timers
- Polling a device by checking its state at regular intervals when the hardware can’t fire interrupts.
- User wants to send some message to other device at regular intervals.
- Send error when some action didn’t happened in particular time period.
- Etc.

# Kernel Timer API
Linux Kernel provides the driver to create timers which are not periodic by default, register the timers and delete the timers.

We need to include the <linux/timer.h> (#include <linux/timer.h>) in order to use kernel timers. Kernel timers are described by the timer_list structure, defined in <linux/timer.h>:

struct timer_list{
/*..............*/
unsigned long expires;
void (*function)(unsigned long);
unsigned long data;
};

The expires field contains the expiration time of the timer (in jiffies). On expiration, function() will be called with the given data value.

## Initialize / Setup Kernel Timer
There are multiple ways to Initialize / Setup Kernel Timer. We’ll see one by one.

### init_timer
void fastcall init_timer ( struct timer_list * timer);

This function is used to initialize the timer. init_timer must be done to a timer prior calling any of the other timer functions. If you are using this function to initialize the timer, then you need to set the callback function and data of the timer_list structure manually.

### setup_timer
void setup_timer(timer, function, data);

Instead of initializing timer manually by calling init_timer, you can use this function to set data and function of timer_list structure and initialize the timer. This is recommended to use.
### DEFINE_TIMER
DEFINE_TIMER(_name, _function, _expires, _data)

If we are using this method, then no need to create the timer_list structure in our side. Kernel will create the structure in the name of _name and initialize it.

## Start a Kernel Timer

### add_timer
void add_timer(struct timer_list *timer);

This will start a timer.

## Modifying Kernel Timer’s timeout

### mod_timer
int mod_timer (struct timer_list * timer, unsigned long expires);

This function is used to modify a timer’s timeout. This is a more efficient way to update the expire field of an active timer (if the timer is inactive it will be activated).

mod_timer(timer, expires) is equivalent to:
del_timer(timer); timer->expires = expires; add_timer(timer);

## Stop a Kernel Timer
These below functions will be used to deactivate the kernel timers.

### del_timer
int del_timer (struct timer_list * timer);
This will deactivate a timer. This works on both active and inactive timers.
### del_timer_sync
int del_timer_sync (struct timer_list * timer);

This will deactivate a timer and wait for the handler to finish. This works on both active and inactive timers.

## Check Kernel Timer status

### timer_pending
int timer_pending(const struct timer_list * timer);

This will tell whether a given timer is currently pending, or not. Callers must ensure serialization wrt. other operations done to this timer, eg. interrupt contexts, or other CPUs on SMP.

# Device Driver Source Code
1. Initialize the timer and set the time interval
2. After timeout, registered timer callback will be called.
3. In the timer callback function again we are re-enabling the timer. We have to do this step if we want periodic timer. Otherwise we can ignore this.
4. Once we done, we can disable the timer.

driver.c

# Building and Testing Driver
- Build the driver by using Makefile (sudo make)
- Load the driver using sudo insmod driver.ko
- Now see the Dmesg (dmesg)

linux@khan: dmesg
[ 2253.635127] Device Driver Insert…Done!!!
[ 2258.642048] Timer Callback function Called [0]
[ 2263.647050] Timer Callback function Called [1]
[ 2268.652684] Timer Callback function Called [2]
[ 2273.658274] Timer Callback function Called [3]
[ 2278.663885] Timer Callback function Called [4]
[ 2283.668997] Timer Callback function Called [5]
[ 2288.675109] Timer Callback function Called [6]
[ 2293.680160] Timer Callback function Called [7]
[ 2298.685771] Timer Callback function Called [8]
[ 2303.691392] Timer Callback function Called [9]
[ 2308.697013] Timer Callback function Called [10]
[ 2313.702033] Timer Callback function Called [11]
[ 2318.707772] Timer Callback function Called [12]

- See the timestamp. That callback function is executing every 5 seconds.
- Unload the module using sudo rmmod driver

# Points to remember
This timer callback function will be executed from interrupt context. If you want to check that, you can use function in_ interrupt( ), which takes no parameters and returns nonzero if the processor is currently running in interrupt context, either hardware interrupt or software interrupt. Since it is running in interrupt context, user cannot perform some actions inside the callback function mentioned below.

- Go to sleep or relinquish the processor
- Acquire a mutex
- Perform time-consuming tasks
- Access user space virtual memory