I/O Control in Linux
## Introducing an ioctl()

Input-output control (ioctl, in short) is a common operation or system call available with most of the driver categories. It is a “one bill fits all” kind of system call. If there is no other system call, which meets the requirement, then definitely ioctl() is the one to use. Practical examples include volume control for an audio device, display configuration for a video device, reading device registers, … – basically anything to do with any device input / output, or for that matter any device specific operations. In fact, it is even more versatile – need not be tied to any device specific things but any kind of operation. An example includes debugging a driver, say by querying of driver data structures.
Question is – how could all these variety be achieved by a single function prototype. The trick is using its two key parameters: the command and the command’s argument. The command is just some number, representing some operation, defined as per the requirement. The argument is the corresponding parameter for the operation. And then the ioctl() function implementation does a “switch … case” over the command implementing the corresponding functionalities. The following had been its prototype in Linux kernel, for quite some time:

int ioctl(struct inode *i, struct file *f, unsigned int cmd, unsigned long arg);

Though, recently from kernel 2.6.35, it has changed to the following:

long ioctl(struct file *f, unsigned int cmd, unsigned long arg);

If there is a need for more arguments, all of them are put in a structure and a pointer to the structure becomes the ‘one’ command argument. Whether integer or pointer, the argument is taken up as a long integer in kernel space and accordingly type cast and processed.

Ioctl() is typically implemented as part of the corresponding driver and then an appropriate function pointer initialized with it, exactly as with other system calls open(), read(), … For example, in character drivers, it is the ioctl or unlocked_ioctl (since kernel 2.6.35) function pointer field in the struct file_operations, which is to be initialized.

Again like other system calls, it can be equivalently invoked from the user space using the ioctl() system call, prototyped in <sys/ioctl.h> as:

int ioctl(int fd, int cmd, ...);

Here, cmd is the same as implemented in the driver’s ioctl() and the variable argument construct (…) is a hack to be able to pass any type of argument (though only one) to the driver’s ioctl(). Other parameters will be ignored.

Note that both the command and command argument type definitions need to be shared across the driver (in kernel space) and the application (in user space). So, these definitions are commonly put into header files for each space.

### Querying the driver internal variables

To better understand the boring theory explained above, here’s the code set for the “debugging a driver” example mentioned above. This driver has 3 static global variables status, dignity, ego, which need to be queried and possibly operated from an application. query_ioctl.h defines the corresponding commands and command argument type. Listing follows:

#ifndef QUERY_IOCTL_H
#define QUERY_IOCTL_H
#include <linux/ioctl.h>
typedef struct
{
        int status, dignity, ego;
} query_arg_t;
#define QUERY_GET_VARIABLES _IOR('q', 1, query_arg_t *)
#define QUERY_CLR_VARIABLES _IO('q', 2)
#endif

Using these, the driver’s ioctl() implementation in query_ioctl.c would be:

static int status = 1, dignity = 3, ego = 5;
#if (LINUX_VERSION_CODE < KERNEL_VERSION(2,6,35))
static int my_ioctl(struct inode *i, struct file *f, unsigned int cmd,
        unsigned long arg)
#else
static long my_ioctl(struct file *f, unsigned int cmd, unsigned long arg)
#endif
{
        query_arg_t q;
        switch (cmd)
        {
        case QUERY_GET_VARIABLES:
        q.status = status;
        q.dignity = dignity;
        q.ego = ego;
        if (copy_to_user((query_arg_t *)arg, &q,
        sizeof(query_arg_t)))
        {
        return -EACCES;
        }
        break;
        case QUERY_CLR_VARIABLES:
        status = 0;
        dignity = 0;
        ego = 0;
        break;
        default:
        return -EINVAL;
        }

        return 0;
}

And finally the corresponding invocation functions from the application query_app.c would be as follows:

#include <stdio.h>
#include <sys/ioctl.h>
#include "query_ioctl.h"
void get_vars(int fd)
{
        query_arg_t q;
        if (ioctl(fd, QUERY_GET_VARIABLES, &q) == -1)
        {
        perror("query_apps ioctl get");
        }
        else
        {
        printf("Status : %d\n", q.status);
        printf("Dignity: %d\n", q.dignity);
        printf("Ego : %d\n", q.ego);
        }
}
void clr_vars(int fd)
{
        if (ioctl(fd, QUERY_CLR_VARIABLES) == -1)
        {
        perror("query_apps ioctl clr");
        }
}

Do the following to try out:

1. Build the ‘query_ioctl’ driver (query_ioctl.ko file) and the application (query_app file) by running make using the provided Makefile.
2. Load the driver using insmod query_ioctl.ko.
3. With appropriate privileges and command-line arguments, run the application query_app:

(a) ./query_app	# To display the driver variables
(b) ./query_app -c	# To clear the driver variables
(c) ./query_app -g	# To display the driver variables
(d) ./query_app -s	# To set the driver variables (Not mentioned above)

4. Unload the driver using rmmod query_ioctl.

## Defining the ioctl() commands

As per the Portable Operating System Interface (POSIX) standard for ioct l . The standard talks about the 32-bit command numbers being formed of four components embedded into the [31:0] bits:

1. Direction of command operation [bits 31:30] – read, write, both, or none – filled	by the corresponding macro (_IOR, _IOW, _IOWR, _IO)

2. Size of the command argument [bits 29:16] – computed using sizeof() with the	command argument’s type – the third argument to these macros

3. 8-bit magic number [bits 15:8] – to render the commands unique enough –	typically an ASCII character (the first argument to these macros)

4. Original command number [bits 7:0] – the actual command number (1, 2, 3, …),	defined as per our requirement – the second argument to these macros.

“Check out the header <asm-generic/ioctl.h> for implementation details”