Synchronization without Locking

## Atomic Operations

Atomic operations are invisible and uninterruptible. Each of these compile into a single machine instruction as far as possible and are guaranteed to be atomic.In a multiprocessor systems if a program is being executed on multiple processors with data being shared between the processors then the update of data by one one processor might be affected by an update by another processor.For eg consider the instruction val = val + 1; This is a good example of a read modify write instruction where the processor read the value of "val" modifies it and write it back. In a uniproessor system this poses no problem because the processor will not let go of the memory bus until the instruction is not completely executed. But in a multiprocessor system, the memory bus might be released after the read and while one processor updates the value another processor can make use of the bus. If two processors, processor A and processor B reach this instruction at the same time. Assume the value of val is 3 initially. Processor A reads the value 3 and lets go of the bus
While processor A updates the val processor B also reads val as 3 and lets the go of the bus
Now processor A updates the new value 4 in the val
Then processor B also updates the value of val as 4. With 2 increments the value of val should have become 5, but it remains at 4 because both the processors were allowed to read the variable before one of them finished the operation on it.
This simultaneous access can be prevented using semaphores and spinlocks but implementing a semaphore or spinlock for one instruction might be an overkill.

There is another solution in linux kernel called atomic variables
Atomic variables are the ones on whom the read modify write operation is done as one instruction with out any interruption .To make use of the atomic variables the variable needs to be declared as of type atomic_t.
Kernel provides a atomic integer type atomic_t for atomic operations. Below are the operations:

#include <asm/atomic.h>
atomic_t *val   Declaration
atomic_read(val): Returns the value of *val
atomic_set(val,i) :  Sets *val to i
atomic_add(i,val):    adds i to *val
atomic_sub(i,val):  Subtracts i from *val
atomic_sub_and_test(i, val) : Subtracts i from *val and returns 1 if the result is zero,
atomic_inc(val) : Adds 1 to *val
atomic_dec(val) :  Subtracts 1 from *val
atomic_dec_and_test(val): Subtracts 1 from *val and returns 1 if the result is zero, otherwise it returns 0
atomic_inc_and_test(val): Adds 1 to *v and returns 1 if the result is zero; 0 otherwise
atomic_add_negative(i, val): Adds i to *val and returns 1 if the result is negative, otherwise it returns 0
atomic_inc_return(val): Adds 1 to *val and returns the new value of *val
atomic_dec_return(val): Subtracts 1 from *val and return the new value of *val
atomic_add_return(i, val) : Adds i to *val and returns the new value of *val
atomic_sub_return(i, val): Subtracts i from *val and return the new value of *val
void atomic_set(atomic_t *a, int i); // Set the atomic variable a to integer value i
int atomic_read(atomic *a); // Return the value of atomic variable a
void atomic_add(int i, atomic_t *a); // Add i to atomic variable a
void atomic_sub(i, atomic_t *a); // Subtract i from atomic variable a
void atomic_inc(atomic_t *a); // Increment operation
void atomic_dec(atomic_t *a); // Decrement operation

## Atomic Bit Operations

Many a times, the requirement is to flag some condition. For this, a single bit may serve the purpose well. However, atomic_t type variable doesn’t work well for manipulating the bits. For this, the kernel provides a set of operations as listed below:
#include <asm/bitops.h>
void set_bit(int nr, void *a); // Set the bit number nr in value pointed by a
void clear_bit(int nr, void *a); // Clear the bit number nr in value pointed by a
void change_bit(int nr, void *a); // Toggle the bit at position nr

Example 1 showing the programing part